## Slide 2
For a 15 kW household range, ___ W is the demand load.
  15,000
  12,000
  9200
  8400
    NEC® Reference: Table 220.55

## Slide 3
A ___ A circuit breaker would be required for OCP for a #6 TW Cu conductor.
  55
  60
  50
  56
    NEC® Reference: 240.4(B)(2); Table 310.15(B)(16)

## Slide 4
A motor-feeder circuit with a 5 HP, 208 V motor and two 1 1/2 HP single-phase motors would require a ___ A circuit breaker for OCP.
  80
  90
  100
  110
    NEC® Reference: 430.248; 430.62(A)

## Slide 5
Type NM cable is permitted to pass through a section of studs used for A/C air return provided that it ___.
  passes through perpendicularly
  is supported every 36"
  is installed vertically
  none of the above
    NEC® Reference: 300.22(C), Ex.

## Slide 6
Number 12 Type NM Cu cable used for derating has an ampacity of ___ A.
  15
  25
  30
  16
    NEC® Reference: Table 310.15(B)(16); 334.80